## Slide 1
In-cylinder air flow structure makes significant impacts on fuel spray dispersion, fuel mixture formation, and flame propagation in spark ignition direct injection (SIDI) engines. While the flow field patterns and their transient characteristics are difficult to identify due to diversity, deep learning techniques, based on convolutional neural network (CNN) and recurrent neural network (RNN) models, can extract these specific features in an intuitive and efficient way.
OBJECTIVES
Vortex structure recognition and analysis:
  Vortex center location, rotation direction and size.
Flow field movement prediction:
  Predict flow field movement based on data of previous flow fields.
UM-SJTU Joint Institute, Shanghai Jiao Tong University
Author: Fengnian Zhao, Zhiming Ruan, Chen Guo, Penghui Ge
Advisor: David Hung
Application of Machine Learning and Artificial Intelligence Techniques on Velocity Flow Field Pattern Recognition and Prediction
EXPERIMENTAL SETUP AND SCHEMATIC
Optical Engine
PIV* measurements
*PIV: Particle image velocimetry, which is using the particle displacement between two temporally adjacent frames of a image pair to calculate gas phase flow motion velocity distribution.
RESEARCH BACKGROUND
VORTEX RECOGNITION
R-CNN (Region with Convolutional Neural Network Feature) model
R-CNN model:
Size of input image: 25×25. Size of ROI: 7×7.
Two CNN models ( one to judge whether there is a vortex center, and the other to identify the location and direction)
Vortex Center & Direction Identification
Vortex Size Recognition
Result: The R-CNN model can identify
general complete vortexes
incomplete vortexes
vortexes whose centers are very close to the edge of the image or outside the image
region whose shape is like a vortex, but the magnitude and direction details are not satisfied
Treat flow fields as two grayscale images
Extract the whole image into blocks of size as region of interest (ROI)
R-CNN model:
Size of input image: 25×25. Size of ROI: 5×5.
One CNN models to decide whether it is a part of a vortex.
X-axis
Y-axis
Input image
All blocks checked
Region of Interest (ROI)
Extract the first block
Move to next block
Check the feature of ROI with CNN models and output corresponding label
No
Yes
A matrix of all output labels
Integrate & analyze information
Result: The model works perfect for general vortexes and can identify some special vortex centers which is close to the edge of the image.
A special case:
Incomplete vortex
CONTRIBUTION
R-CNN models can recognize the location, direction and size range of the vortexes in a flow field very well.
R-CNN models considers more on the general shape of the image than the detailed velocity magnitude and direction, which may cause some errors.
The deep learning methodology to predict the flow field movement is fast and accurate once the model is full-trained. It can be adapted to real engines which could control intake fluid to avoid energy drain based on the prediction given by the model.
The prediction model can also be used to overcome limits on experimental equipment. It can be applied as a data-mining method which generates more data at different time steps based on data we already have.
FLOW FIELD PREDICTION
METHODOLOGY
PROCESSES
True flow field
Predicted flow field
Reverse convolution
RNN(Recurrent Neural Network):
RNN model is a deep learning model that has memory. It can take sequential inputs and perform prediction or classification on more than one inputs.
Autoencoder:
Autoencoder will be applied to compress the input flow fields with least amount of drains on information so that them can be represented by 1D vectors with smaller size.
Generally, prediction loss is very small. But the prediction about vectors that have small magnitude is not so good as that on vectors with great magnitude.
Autoencoder:
RESULT AND DISCUSSION
Sequential flow field inputs
Compressed vector representation
Compressed vector representation
Final predicted flow field
By autoencoder
By RNN
By Reconstructor
3D matrix
1D vector
Flatten
Several neural network layers
Smaller 1D vector
3D matrix
Note: We want the final output close to the input as much as possible!
Prediction:
METHODOLOGY
PROCESSES
RESULT AND DISCUSSION
CONTRIBUTION
ACKNOWLEDGMENT
The experimental work is implemented in the Institute of Automotive Engineering of Shanghai Jiao Tong University and sponsored by General Motors Global R&D.